## Slide 1
VAST Data
Network Training
Node Networking · Network Design · L2/L3 Topologies
Created by Wong Tran

## Slide 2
Agenda
01
CNode Networking
Front end & backend interfaces, SR-IOV, bond config, VLAN 69, client VIPs
02
EBox Networking
Identical architecture to CNode — expansion box for additional storage
03
DNode Networking
Backend-only interfaces, no front end NIC, BlueField DPU management
04
Converged vs Split Design
How VAST node NICs connect to the switching fabric
05
L2/L3 Topologies
Small (pair), Medium (spine-leaf), Large (EVPN-BGP) deployment patterns

## Slide 3
01
CNode Networking
Front end & backend interfaces, SR-IOV virtual functions,
bond configuration, VLAN 69 sub-interfaces, and client VIPs

## Slide 4
CNode — Interface Overview (Dual NIC)
CBox 1U chassis — 4 PCIe buses, 8 physical functions, 2 virtual functions
Front End Interface
Data plane — client VIPs
enp65s0f0 · enp65s0f1
Backend Interface
Cluster mesh — SR-IOV + bond
enp1s0f0 · enp1s0f1 (PF)
enp1s0f2 · enp1s0f3 (VF)
Gigabit Interface
Management / spare
enp194s0f0 (mgmt)
enp194s0f1, enp193s0f0, enp193s0f1
Configuration Variants
Dual NIC + Mgmt via Gigabit
Default — FE NIC for VIPs, mgmt on enp194s0f0
Dual NIC + Mgmt via Bond
Management IP on bond0 instead of gigabit
Single NIC + Mgmt via Gigabit
No FE NIC — VIPs on backend PFs directly
Single NIC + Mgmt via Bond
No FE NIC — VIPs on backend PFs, mgmt on bond0

## Slide 5
CNode — SR-IOV Architecture
ConnectX-7 dual-port NIC with hardware virtualization for HA failover
Physical Port 0
enp1s0f0 — PF
↓ VF
enp1s0f2 — VF (SR-IOV)
Physical Port 1
enp1s0f1 — PF
↓ VF
enp1s0f3 — VF (SR-IOV)
ACTIVE
BACKUP
bond0 — active-backup (mode 1)
Key Details
• PFs carry direct VLAN 69 sub-interfaces for low-latency cluster mesh
• VFs are bonded (active-backup) for HA failover — 200 Gbps per VF
• MII polling interval: 100ms — locally administered MAC addresses
• Bond runs on VFs so PFs remain free for direct cluster mesh paths

## Slide 6
CNode — VLAN 69 Cluster Mesh Paths
3 independent paths into VLAN 69 for maximum resilience
Path A — PF0 Direct
Direct path via Physical Function 0
Interface
enp1s0f0.69
Lab IP
172.16.1.11/24
Production Subnet
172.16.0.0/18
Path B — PF1 Direct
Direct path via Physical Function 1
Interface
enp1s0f1.69
Lab IP
172.16.2.11/24
Production Subnet
172.16.64.0/18
Bond Path
HA bond path via VF pair (active-backup)
Interface
bond0.69
Lab IP
172.16.3.11/24
Production Subnet
172.16.128.0/18
⚠ Production uses /18 subnets, not /24. Lab uses /24 with 172.16.{1,2,3}.x addressing for the 3 paths.

## Slide 7
CNode — Client VIP Distribution
~74 client VIPs load-balanced across both front-end data plane ports
39
IPs on enp65s0f0
Port 0 — Active data plane
35
IPs on enp65s0f1
Port 1 — Active data plane
VIP Subnets
172.200.0.0/16
10.10.0.0/16
192.168.x.0/24
Key Points
• VIPs distributed roughly evenly across both data plane ports
• Same subnets appear on both ports — VAST load-balances VIP assignments per-port
• Multiple IPs per interface via Linux secondary addresses (no VLAN tags in lab)
• Production: Customers typically use VLANs to segregate client subnets
• L3 routing via upstream switch SVI/IRB interfaces, not L2 segmentation

## Slide 8
CNode — Hardware & Bond Status
$ lshw -c network -businfo
pci@0000:c1:00.0 enp193s0f0 Intel Corp
pci@0000:c1:00.1 enp193s0f1 Intel Corp
pci@0000:c2:00.0 enp194s0f0 Intel Corp
pci@0000:c2:00.1 enp194s0f1 Intel Corp
pci@0001:01:00.0 enp1s0f0 ConnectX-7
pci@0001:01:00.1 enp1s0f1 ConnectX-7
pci@0001:01:00.2 enp1s0f2 ConnectX-7 VF
pci@0001:01:00.3 enp1s0f3 ConnectX-7 VF
pci@0001:41:00.0 enp65s0f0 ConnectX-7
pci@0001:41:00.1 enp65s0f1 ConnectX-7
$ cat /proc/net/bonding/bond0
Mode: fault-tolerance (active-backup)
Primary Slave: None
Active Slave: enp1s0f2
MII Polling: 100 ms
Slave: enp1s0f2 (ACTIVE)
Speed: 200000 Mbps Duplex: full
MAC: 4a:cb:92:8a:b1:54
Slave: enp1s0f3 (BACKUP)
Speed: 200000 Mbps Duplex: full
MAC: a2:ae:c4:a3:de:81
10 network devices across 4 PCIe buses · 2 VFs bonded at 200 Gbps each · 3 VLAN 69 sub-interfaces · ~74 client VIPs

## Slide 9
Single NIC vs Dual NIC
Dual NIC
Front End NIC (2 ports)
enp65s0f0, enp65s0f1
→ Dedicated to client VIPs only
Backend NIC (2 ports + 2 VFs)
enp1s0f0/1 (PF), enp1s0f2/3 (VF)
→ Cluster mesh via VLAN 69
Total: 10 devices, 4 PCIe buses
Separate data plane & cluster mesh paths
Single NIC
No Front End NIC
enp65s0f0/1 do not exist
→ VIPs assigned to backend PFs
Backend NIC (2 ports + 2 VFs)
enp1s0f0/1 carry VIPs + mesh
→ SR-IOV separates VIP from mesh
Total: 8 devices, 3 PCIe buses
Shared NIC — traffic separated via SR-IOV

## Slide 10
02–03
EBox & DNode Networking
EBox mirrors CNode architecture · DNode is backend-only (no front end NIC)

## Slide 11
DNode — Key Differences from CNode/EBox
DNodes serve storage only — no front end interfaces, no client VIPs
Feature | CNode / EBox | DNode
Front End NIC | enp65s0f0 / enp65s0f1 ConnectX-7 (client VIPs) | None DNodes have no front end
Backend NIC | enp1s0f0 / enp1s0f1 + VFs enp1s0f2/3 | enp3s0f0 / enp3s0f1 + VFs enp3s0f2/3
Gigabit Mgmt | enp194s0f0 (direct IP) 10.143.11.204/16 | enp9s0 + VLAN sub-ifs VLAN 70/71/99 + tmfifo_net0
VLAN 69 IPs | 172.16.{1,2,3}.11/24 | 172.16.{1,2,3}.112/24
BlueField DPU | N/A | tmfifo_net0 169.254.102.2/30 (BMC access)
Chassis | CBox/EBox 1U | DBox — 2 DNodes per box
DNode uses BlueField DPU with tmfifo_net0 for out-of-band BMC management at 169.254.102.2/30

## Slide 12
04
Converged vs Split
How VAST node NICs connect to the switching fabric —
the foundation of your network design

## Slide 13
Network Design Options
Converged
Dual NIC
Cisco EBox Only
Frontend & backend NICs both connect to the same VAST leaf pair. Customer switches uplink to VAST leafs.
Benefits
Fewer switches · Simpler cabling · Lower cost
Considerations
Shared bandwidth · Switch failure impacts both traffic types
Converged
Single NIC
CBox / EBox
Backend NIC only — VIPs & cluster mesh share one NIC via SR-IOV. PF carries mesh, VF carries VIPs.
Benefits
Minimum hardware · No frontend NIC needed
Considerations
All traffic on one NIC · Requires SR-IOV
Split
All Platforms
Separate domains: Frontend NIC → customer switches (VIPs), Backend NIC → VAST leaf pair (cluster mesh).
Benefits
Traffic isolation · Independent failure domains
Considerations
More switches · Complex cabling · Higher cost

## Slide 14
Converged — Dual NIC Topology
⚠ Cisco EBox Only
Client Servers (NFS/SMB/S3)
Customer SW-1 (MLAG)
Customer SW-2 (MLAG)
VAST Switching Domain
VAST Leaf-1 (MLAG)
VAST Leaf-2 (MLAG)
VAST Server
Frontend NIC
Backend NIC
Client VIPs ↓
↑ uplinks (cross-connected)
VIP traffic ↑
Cluster mesh ↑

## Slide 15
Converged — Single NIC Topology
Backend NIC only — SR-IOV separates VIP from mesh traffic on the same NIC
Client Servers
Customer SW-1
Customer SW-2
VAST Switching Domain
VAST Leaf-1
VAST Leaf-2
VAST Server
Backend NIC — VIPs (via SR-IOV VF) + Cluster Mesh (PF)
SR-IOV
PF → Cluster mesh
VF → Client VIPs

## Slide 16
Split Topology — Separate Domains
Independent switching domains for VIP traffic and cluster mesh
Customer Domain
Client Servers
Customer SW-1
Customer SW-2
VAST Server
Frontend NIC → VIPs
Backend NIC → Mesh
VAST Backend Domain
VAST Leaf-1
VAST Leaf-2
Separate switching domains — independent failure, dedicated bandwidth per traffic type

## Slide 17
05
L2 / L3 Topologies
Standard VAST Data fabric patterns — Small (pair), Medium (spine-leaf), Large (EVPN-BGP)

## Slide 18
Deployment Size Categories
S
Small — L2 — Pair Switches
Simple MLAG switch pair without a spine layer. Cluster won't exceed port count of a single leaf pair.
2 VAST switches
M
Medium — L2 — Spine-Leaf
Spine-leaf fabric with MLAG. Cluster won't exceed port count of the spine pair. Full mesh leaf↔spine.
2 Spines + 4 Leaves
L
Large — L3 — EVPN-BGP (VXLAN)
BGP underlay + VXLAN overlay for 100+ node clusters. 3 spines for odd-number quorum. Scalable.
3 Spines + N Leaves
Each size supports two uplink modes:
Isolated — VAST fabric not connected to customer network (Split design) Connected — VAST spines/leafs cross-connect to customer switches (Converged)

## Slide 19
Small — Pair Switches (L2)
Isolated (Split)
Customer MLAG Pair
VAST MLAG Pair
VAST EBox / CBox servers
FE NIC → Customer switches
BE NIC → VAST MLAG pair
No cross-connect between domains
Connected (Converged)
Customer MLAG Pair
↕ cross-connect
VAST MLAG Pair
VAST EBox / CBox servers
Both NICs → VAST MLAG pair
Customer SWs uplink to VAST pair
Simpler, fewer switches overall

## Slide 20
Medium & Large Topologies
Medium — L2 Spine-Leaf
• 2 Spine switches + 4 Leaf switches
• Full mesh: each leaf uplinks to both spines
• MLAG active-active forwarding with ISL failover
• Servers dual-home to both switches in each leaf pair
• Isolated: fabric not connected to customer network
• Connected: spines cross-connect to customer MLAG
Large — L3 EVPN-BGP
• 3 Spine switches (odd-number quorum)
• BGP underlay + VXLAN overlay
• Full mesh: each leaf peers with all 3 spines
• Scalable to 100+ nodes
• Isolated: completely separate from customer fabric
• Connected: 6 BGP sessions (3 spines × 2 customer SWs)
Failure Scenarios & Redundancy
Switch Fails
MLAG partner takes over all forwarding. Servers dual-homed to both — retain connectivity.
Spine Fails
Remaining spine(s) carry full load. Leaf-to-leaf still reachable via surviving spines.
Single Cable Fails
Server retains connectivity via other NIC to partner switch. MLAG handles re-routing.
Server NIC Fails
Bond failover to backup VF. Active-backup mode 1 switches within 100ms MII polling.

## Slide 21
Design Mapping Summary
How Converged/Split designs map to L2/L3 topology uplink modes
Network Design | Uplink Mode | Topology Sizes | Platform Support
Split | Isolated | Small · Medium · Large | All platforms
Converged — Dual NIC | Connected | Small · Medium · Large | Cisco EBox only
Converged — Single NIC | Connected | Small · Medium · Large | CBox · EBox
Key Takeaways
Split (Isolated) provides maximum traffic isolation — separate switching domains for VIP and cluster mesh
Converged (Connected) reduces switch count and cabling complexity — both traffic types share VAST leaf pair
SR-IOV enables Single NIC converged — PF carries cluster mesh, VF carries client VIPs with bond failover
VLAN 69 provides 3 independent cluster mesh paths (PF0 direct, PF1 direct, bond) for resilience
All topologies support MLAG active-active forwarding with ISL failover for high availability
Production uses /18 subnets for VLAN 69 addressing — lab environments use /24 for simplicity

## Slide 22
Thank You
VAST Data — Network Training
Node Networking · Converged vs Split · L2/L3 Topologies
Created by Wong Tran